NEW  INSTALLATIONS ON THE WHOLE REGIONAL TERRITORY

INDICATIVE TABLE FOR THE ADJUSTMENTS OF OUTDOOR LIGHTING INSTALLATIONS ACCORDING TO R.L. N.17/00 OF THE LOMBARDIA REGION AND RELATED REGULATION

| VIOLATION ASSESSMENT FORM | N. |  |
| --- | --- | --- |

| Locality/Street |  |
| --- | --- |
| Town |  |
| VERIFIED VIOLATION | RECOMMENDED ADJUSTMENT |
| Lighting devices – Maximum Light Intensity Allowed 0cd/klm at 90° and beyond (art.6, commas 2 & 5) |
| Not full cut-off with protruding lamp and/or not transparent glass (spheres, lanterns, street lamps, road armours, projectors) |  | Replacement option: with full cut-off optics and lamp recessed in the upper part of the device if possible, replace the cup with horizontal flat glass |
| full cut-off Devices with wrong inclination and light dispersion |  | Modify the inclination Insert a shield in the upper part |
| Lamps - High efficiency (art.6, comma 2) |
| Low efficiency lamp such as mercury-vapours lamps or fluorescence lamps |  | Replace with high efficiency lamps >100 lm/W such as high- or low-pressure sodium lamps |
| Illuminated surfaces (art.6, comma 2) |
| Minimum level of mantained average luminance higher than that indicated by the safety rules |  | Reduce the installed power |
| Signboards without their own lighting (art.6, comma 4) |
| Illuminated from the bottom towards the top |  | Replace with lighting from the top towards the bottom |
| Monuments and buildings (art.6, comma 10) |
| Generic monuments and buildings illuminated from the bottom towards the top |  | Replace with lighting from the top towards the bottom |
| Subjects of proved historical and architectural value illuminated from the bottom towards the top with light beams oriented beyond the edges of the structure |  | Replace with lighting from the top towards the bottom reorient the beams of light one meter under the upper edge of the structure and within its perimeter |
| Total or partial switch off |  | Within 24.00 hours |
| Flow reducers (art.6, comma 2) |
| New installations not realized with flow reducer |  | Insert a system for the reduction of the flow not lower than 30%, within the hours 24 |
| Installations equipped with flow reducers which intervene after the hours 24, and/or reductions of the flow higher than 30% |  | Adjust the regulator of the light flow to intervene within the hours 24 and with a maximum residual flow of 30%. |
| Beacons (art.6, comma 10) |
| Rotary or fixed beacons for pure advertising purposes have been installed |  | Immediate removal |

PRE-EXISTENT INSTALLATIONS IN THE PROTECTED AREAS

INDICATIVE TABLE FOR THE ADJUSTMENTS OF OUTDOOR LIGHTING INSTALLATIONS ACCORDING TO R.L. N.17/00 OF THE LOMBARDIA REGION AND RELATED REGULATION

| VIOLATION ASSESSMENT FORM | N. |  |
| --- | --- | --- |

| Locality/Street |  |
| --- | --- |
| Municipality |  |
| VERIFIED VIOLATION | RECOMMENDED ADJUSTMENT |
| Within 4 years from coming into force of the law (art.9, comma 1) |
| Lamps - High efficiency (art.9, comma 1) |
| Low efficiency lamp such as mercury-vapours lamps or fluorescence lamps |  | Replace with high efficiency lamps >100 lm/W such as high- or low-pressure sodium lamps If the above is not possible, replace the devices |
| Road floodlights - (art.9, comma 2) |
| Installations dispersing more than 0 cd/klm at 90° and beyond |  | replace with full cut-off optics and lamp recessed in the upper part of the device in order to keep the light dispersion less than 0.49 cd/klm at 90° and beyond install suitable shields, replace or remove the optics protective cups with flat glass ( if possible with the lamp recessed in the upper part of the device ) in order to keep the light dispersion less than 0.49 cd/klm at 90° and beyond |
| Urban fittings and higly polluting devices - (art.9, comma 4) |
| higly polluting devices (such as globes, lanterns or similar) dispersing more than 15 cd/klm at 90° and beyond |  | Must be: replaced with devices dispersing max 0.49 cd/klm at 90° and beyond shielded or however equipped with suitable devices to contain and direct to the ground the light flow and provided with transparent protective glasses ) in order to keep the light dispersion less than 0.49 cd/klm at 90° and beyond |
| Beacons, beacon-towers and car parks - (art.9, comma 5) |
| Floodlights dispersing more than 0.49 cd/klm at 90° and beyond |  | Replacement option: must be replaced with devices having the specified parameters (max 0.49 cd/klm at 90° and beyond) If sufficient, and the safety is not compromised, change the inclinations of the floodlights equipping them with horizontal flat glass |
| Signboards of not specific and indispensable nocturnal use - (art.9, comma 4) |
| They are lit after the hours 23 (in winter) and hours 24 (in summer) |  | They must be shut off after the hours 23 (in winter) and hours 24 (in summer) |
| Flow reduction within the hours 23 in winter, hours 24 in summer - (art.9, comma 3) |
| Installations not equipped with light flow reducers |  | Replacement option: without changing the conditions of safety, switching off of 50% of the light sources insertion of a suitable system for the reduction of the light flow |